## Slide 1: Mobile Communication 1G – 5G Evolution
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: References
Kurose and Ross, Book, Computer Networking, A Top down approach, 7th Edition
J. Schiller, Book, Mobile Communication, 2008, Pearson
Multiple Internet presentations

## Slide 3: We will study..
Why should we know about Mobile Technology?
Limited mobility vs full mobility
Brief History of Mobile Networks
Basic concept – Cellular Networks
2G Network – GSM
3G Network
4G Network – LTE Long Term Evolution
5G Network

## Slide 4: Why should we learn about Mobile Technology?

## Slide 5: Mobile has become a very important part of our lives
You can reach almost 81% people on the planet Earth with mobile
Extremely low cost – Almost everyone can afford it
Mobile + Internet = Killer Technology for DT

## Slide 6: It’s like a magic !
Anyplace in the world, I travel, I receive my calls… can do transactions !
How does it work?
How does it know where I am ?

## Slide 7: Let’s learn a little bit about Mobile phone Technology !

## Slide 8: Limited Mobility vs Full Mobility

## Slide 9: Limited Mobility vs Full Mobility
Limited Mobility
Unlimited Mobility – Cellular Networks
Our Interest

## Slide 10: Mobile - Evolution

## Slide 11: Initial Mobiles – Only for Voice
Remember that initial mobile phones were designed only for calls (voice)

## Slide 12: Today’s Mobiles – Millions of Applications
Mobile devices today – A powerful computer that also does voice calls
Support of millions of applications
There are many types of cellular technologies. Let’s first discuss the basics.

## Slide 13: Cellular Network Basics
Cellular networks are based on “Radio Technology”
Radio waves are electromagnetic waves
Your device both generates and receives radio signals
Radio communications are used in many applications
  For different applications, frequency ranges are different
Cell phones operate in this frequency
Logarithmic scale

## Slide 14
Radio Spectrum
Notes: FCC allocates spectrum to users – who are these?
Govt. itself (various agencies), military.
Public-safety.
Broadcasters
Telecommunications providers (aka operators) – license holders.
Different bands behave differently …
Most wave propagation properties are frequency/wave-length dependent:

## Slide 15: What is a cell?

## Slide 16: What is a Cell?
Areas divided into cells
  Each served by its own antenna
  Served by base station consisting of transmitter, receiver, and control unit
  Certain channels (e.g. bands of frequencies) allocated to each cell
  Cells set up such that antennas of all neighbors are approximately equidistant (hexagonal pattern)
  Use multiple low-power transmitters (100 W or less)

## Slide 17: Advantage of Cellular System
Reuse of frequencies in nearby cells
  Adjacent cells assigned different frequencies to avoid interference
f4
f5
f1
f3
f2
f6
f7
f3
f2
f4
f5
f1
Cells with the same number (colour) have the same set of frequencies

## Slide 18: Advantage/Disadvantages of Cellular System
High Capacity
Less transmission power
Reduced Setup time
  Compare this with landline telephone network
Cell size can be changed
Fault tolerance
  Robustness against failure of single component
Handover is required
Frequency planning should be good
  Spectrum is expensive

## Slide 19: Different cell sizes for Rural and Urban

## Slide 20: Cellular Network Evolution: 0G to 5G
0G: Briefcase-size mobile radio telephones
1G: Analog cellular telephony
2G: Digital cellular telephony
3G: High-speed digital cellular telephony (including video telephony)
LTE (4G): IP-based “anytime, anywhere” voice, data, and multimedia telephony at faster data rates than 3G
5G: Enhanced Mobile Broadband (eMBB) – Ultra HD Video, Massive Machine type communication – for smart homes and smart city, Ultra reliable and low latency communication

## Slide 21: Mobile Network Evolution
1G 2G 3G 4G 5G
Mid 1980s 1990s 2000s 2010s 2020s
analog
voice
Digital voice
+ Simple data
Mobile
broadband
Mobile Internet
More & faster
3G
WCDMA/HSPA+
CDMA2000/EVDO
TD-SCDMA
1G
AMPS, NMT
TACS
2G
GSM/GPRS/ EDGE
cdmaOne
4G
LTE
LTE-A
Mobile Internet – Ultra High Speed, Low latency, Machine to machine
5G
LTE Advance Pro NR
Notes: All these are empowered by the evoluation of mobile networks.
Today, the world is advancing to 4G LTE and even LTE advanced.
At this time point, almost everyone knows that 3G/4G mobile networks are everywhere.
This fact can be easily supported by many numbers.
For example, 3G/4G have been deployed in 203 countries; serving 6.8 billions user.
By 2014 (this year), it will go beyond our global population.
Last year, more than half a billion smartphones and tablets are shipped,
The market is $1 trillion by 2016.
And so on…
=========================================================
Mobile network is the largest scale wireless infrastructure.
It covers the whole planet and serves billions of users.
It provides mobile users with data service and carrier-grade quality voice service

## Slide 23: Development of mobile telecommunication systems
1G
2G
3G
2.5G
IS-95
cdmaOne
IS-136
TDMA
D-AMPS
GSM
PDC
GPRS
IMT-DS
UTRA FDD / W-CDMA
EDGE
IMT-TC
UTRA TDD / TD-CDMA
cdma2000 1X
1X EV-DV
(3X)
AMPS
NMT
IMT-SC
IS-136HS
UWC-136
IMT-TC
TD-SCDMA
CT0/1
CT2
IMT-FT
DECT
CDMA
TDMA
FDMA
IMT-MC
cdma2000 1X EV-DO
HSPA
3.9G
4G
LTE
LTE
advanced
5G
Ref: Prof. Dr.-Ing. Jochen H. Schiller

## Slide 24: Basic Concept – Cellular Networks

## Slide 25: Cellular Network - Basics
Base stations:
  Transmit and receive signals from mobiles at given frequency range
  Multiple base stations use the same spectrum (spectral reuse)
  Each mobile is typically serviced by the nearest base station
Cell: The service area of each base station
f4
f5
f1
f3
f2
f6
f7
f3
f2
f4
f5
f1

## Slide 26
Mobile
Switching
Center
Public telephone
network
Mobile
Switching
Center
Components of cellular network architecture
connects cells to wired tel. net.
manages call setup
handles mobility
MSC
Covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network
Ref: Computer Networking Book: Kurose and Ross

## Slide 27: Cellular networks: the first hop
Two techniques for sharing mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
CDMA: code division multiple access
frequency
bands
time slots
Ref: Computer Networking Book: Kurose and Ross

## Slide 28: Handoff !
What happens when a user is mobile?
  Especially when crossing a cell boundary while continuing the call
Handoff (typically 30 msec
  At any time, mobile station (MS) is in one cell and under the control of a BS
  When a MS leaves a cell, BS notices weak signal
  BS asks surrounding BSs if they are getting a stronger signal
  BS transfers ownership to one with strongest signal
  new channel is assigned to the MS and it is notified about new boss
Public
Switched
Telephone
Network
(PSTN)
Mobile
Telephone
Switching
Center
(MTSC)
Cell 1
Cell 2
HLR
VLR

## Slide 29: 2G Network: GSM

## Slide 30
BSC
BTS
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
Legend
2G (voice) network architecture
MSC
Public
telephone
network
Gateway
MSC
G

## Slide 31: GSM Architecture
fixed network
BSC
BSC
MSC
MSC
GMSC
OMC, EIR, AUC
VLR
HLR
NSS (Network Switching
System with OSS
(Operational Support
System)
RSS: Radio
Subsystem
VLR
OMC: Operations and Maintenance center
EIR: Equipment Identity Register
AUC: Authentication Center

## Slide 32: GSM Components - BTS
Transmits and receives signals to/from Mobile Stations
Coverage Area depends on
  Transmitting Power of the BTS
  Transmitting power of the mobile station (user devices)
  Height of the base station antenna
  Obstructions – tall buildings etc
BTS is in the middle of the cell
Uses FDM/TDM communication

## Slide 33: GSM Components – BSC and MSC
Base Station Controller (BSC)
  Services tens of BTSs
  Role
    To allocate BTS radio channels to mobile subscribers (mobile phone)
    Performing paging – Finding the cell in which the mobile user is resident
    Performing handoff
  Base Station Subsystem
    BSC + set of BTSs
Mobile Switching System (MSC)
  User authorization and Accounting
  Call establishment and teardown
  Handoff management
  A cellular provider’s network has multiple MSCs
    Gateway MSCs – connect to larger public telephone network

## Slide 34: GSM Components – HLR, VLR
Databases
Home Location Register (HLR)
  Central master database containing user data, permanent and semi-permanent data of all subscribers assigned to the HLR
  One provider can have several HLRs
Visitor Location Register (VLR)
  Local database for a subset of user data, including data about all user currently in the domain of the VLR

## Slide 35: Mobile Terminated Call
PSTN
calling
station
GMSC
HLR
VLR
BSS
BSS
BSS
MSC
MS
1
2
3
4
5
6
7
8
9
10
11
12
13
16
10
10
11
11
11
14
15
17
1: calling a GSM subscriber
2: forwarding call to GMSC
3: signal call setup to HLR
4, 5: request MSRN from VLR
6: forward responsible (destn) MSC addr to GMSC
7: forward call to
current MSC
8, 9: get current status of MS
10, 11: paging of MS
12, 13: MS answers
14, 15: security checks
16, 17: set up connection
MSRN: Mobile Station Roaming Number – Assigned by visitor-network to mobile
when it roams in another area. It is stored in HLR.

## Slide 36: Performance characteristics of GSM (wrt. analog sys.)
Communication
  mobile, wireless communication; support for voice and data services
Total mobility
  international access, chip-card enables use of access points of different providers
Worldwide connectivity
  one number, the network handles localization
High capacity
  better frequency efficiency, smaller cells, more customers per cell
High transmission quality
  high audio quality and reliability for wireless, uninterrupted phone calls at higher speeds (e.g., from cars, trains)
Security functions
  access control, authentication via chip-card and PIN

## Slide 37: 2G limitations
No Internet (Data) connectivity
In 2.5G Network, GPRS for data communication was introduced

## Slide 38: 1G to 3G
Enabling Technologies
AMPS
GSM
IS-95
GPRS
CDMA-2000
1XRTT
EDGE
CDMA2000
3XRTT
(UMTS)
2.5G
3G
2G
2 Mbps
500 kbps
150 Kbps
100 Kbps
50 Kbps
10 Kbps
1999
2000
2001
2002
2003
TDMA Migration
1G-2G Migration
CDMA Migration
1980
1G
1 Kbps
W-CDMA
(UMTS)

## Slide 39: GSM Evolution to 3G
GSM
9.6kbps (one timeslot)
GSM Data
Also called CSD
GSM
General Packet Radio Services
Data rates up to ~ 115 kbps
Max: 8 timeslots used as any one time
Packet switched; resources not tied up all the time
Contention based. Efficient, but variable delays
GSM / GPRS core network re-used by WCDMA (3G)
GPRS
HSCSD
High Speed Circuit Switched Data
Dedicate up to 4 timeslots for data connection ~ 50 kbps
Good for real-time applications c.w. GPRS
Inefficient -> ties up resources, even when nothing sent
Not as popular as GPRS (many skipping HSCSD)
EDGE
Enhanced Data Rates for Global Evolution
Uses 8PSK modulation
3x improvement in data rate on short distances
Can fall back to GMSK for greater distances
Combine with GPRS (EGPRS) ~ 384 kbps
Can also be combined with HSCSD
WCDMA

## Slide 40: 3G Network

## Slide 41
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
GGSN
G
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
core network
General Packet Radio Service
(GPRS) Core Network
public
Internet
radio interface
(WCDMA, HSPA)
3G (voice+data) network architecture
SGSN: Service GPRS Support Node
GGSN: Gateway GPRS Support Node

## Slide 42: 3G Network
Based on consideration of use of existing 2G infrastructure
  Add parallel infrastructure for data communication
Evolved version of GPRS
It uses Direct Sequence Widespread CDMA within TDMA slots
Data Services associated with WCDMA specification are known as HSPA (High Speed Packet Access)
  Downlink speed : up to 14 Mbps

## Slide 43: 3G (voice+data) network architecture
Serving GPRS support Nodes (SGSNs)
  Responsible for delivering packets to/from the mobile nodes in the radio access network to which SGSN is attached
  SGSN interacts with MSC for that area providing
    User authorization, handoff
    Maintaining user location (cell) information about active mobile nodes
  Forwards packets between mobile nodes and GGSN
Gateway GPRS Support Nodes (GGSNs)
  Acts as a Gateway
    Connects multiple SGSNs to the larger Internet
  For outside world, GGSN looks like any other gateway router
  Mobility of the 3G mobile nodes within GGSN is hidden from the outside world
GPRS: Generalized Packet Radio Service

## Slide 44: 3G (voice+data) network architecture
3G standard: UMTS (Universal Mobile Telecommunication Service(
Radio Network Controller (RNC)
  Controls several cell base transceiver stations (BTSs)
  Connects to circuit switched voice network via MSC
  Connects to packet switched Internet via SGSN
Common first/last hop radio access network
3G UMTS uses CDMA technique known as – Direct Sequence Wideband CDMA (DS-WCDMA)
The data service – HSP (High Speed Packet Access)
  Downlink data rate – 14 Mbps

## Slide 45: 4G Network

## Slide 46: 3G vs 4G
3G and earlier maintains two data paths
  Circuit switched: Phone calls (8kbps) and SMS/MMS
  Packet switched: All IP data

## Slide 47: 3G vs 4G
4G - LTE uses “all in one” approach
  Everything over IP, including voice
  S-GW (Serving Gateway) replaced SGSN, P-GW replaces GGSN

## Slide 48
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
G
3G versus 4G LTE network architecture
GGSN
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
MME
Public
Internet
P-GW
G
S-GW
G
HSS
3G
4G-LTE

## Slide 49
4G: differences from 3G
All IP core: IP packets tunneled (through core IP network) from base station to gateway
no separation between voice and data – all traffic carried over IP core to gateway
Separate control plane and data plane
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
Public
Internet
P-GW
G
S-GW
G
UE
(user element)
eNodeB
(base station)
Packet data
network
Gateway
(P-GW)
Serving
Gateway
(S-GW)
data
MME
HSS
Mobility
Management
Entity (MME)
control
Home Subscriber
Server(HSS)
(like HLR+VLR)

## Slide 50: Elements of 4G LTE architecture
Mobile device
(UE)
Base station
(eNode-B)
radio access
network
all-IP Enhanced Packet Core (EPC)
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
to
Internet
…
Mobile device:
smartphone, tablet, laptop, IoT, ... with 4G LTE radio
64-bit International Mobile Subscriber Identity (IMSI), stored on SIM (Subscriber Identity Module) card
LTE jargon: User Equipment (UE)
OFDM: Orthogonal Frequency Division Multiplexing

## Slide 51: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Base station:
at “edge” of carrier’s network
manages wireless radio resources, mobile devices in its coverage area (“cell”)
coordinates device authentication with other elements
similar to WiFi AP but:
  active role in user mobility
  coordinates with nearly base stations to optimize radio use
LTE jargon: eNode-B

## Slide 52: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Home Subscriber Service
stores info about mobile devices for which the HSS’s network is their “home network”
works with MME in device authentication

## Slide 53: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Serving Gateway (S-GW), PDN Gateway (P-GW)
lie on data path from mobile to/from Internet
P-GW
  gateway to mobile cellular network
  Looks like nay other internet gateway router
  provides NAT services
other routers:
  extensive use of tunneling

## Slide 54: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Mobility Management Entity
device authentication (device-to-network, network-to-device) coordinated with mobile home network HSS
mobile device management:
  device handover between cells
  tracking/paging device location
path (tunneling) setup from mobile device to P-GW

## Slide 55: 5G Network

## Slide 56: On to 5G!
Goal: 10x increase in peak bitrate, 10x decrease in latency, 100x increase in traffic capacity over 4G
5G NR (new radio):
  two frequency bands: FR1 (450 MHz–6 GHz) and FR2 (24 GHz–52 GHz): millimeter wave frequencies
  MIMO: multiple directional antennae
Millimeter wave frequencies: much higher data rates, but over shorter distances
  pico-cells: cells diameters: 10-100 m
  massive, dense deployment of new base stations required

## Slide 57
https://www.itu.int/dms_pubrec/itu-r/rec/m/R-REC-M.2083-0-201509-I!!PDF-E.pdf

## Slide 58: 5G use cases
Massive Machine-to-Machine (M2M) communication
  Support for billions of IoT devices
Ultra Reliable low latency communication
  Support for mission critical real-time communication
    Safety systems
    Autonomous Driving
    Industrial Robotics
    Etc
Enhanced Mobile Network
  High Data Speed
  Peak data rates up to 20 Gbps

## Slide 59: Lecture Summary
Mobile Technology has changed the world of Telecommunication
Along with Internet, it has caused significant digital penetration
With 5G Technology, end users will be able to use highspeed data (Internet) communication with very low delays
  It will allow massive machine to machine communications – required for IoT