## Slide 1: Lecture 10: The Internet Technologies – Part 2 Connecting to a website, World Wide Web
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Contents
How do you connect to a website
IP packet routing
End-to-end protocols
WWW basics

## Slide 3: How do you connect to a website ?

## Slide 4: Basic lower layer technologies for Interconnection to the Internet
Internet works over link layer technologies
One of the following must be present
  Ethernet
  Wireless Ethernet, WiFi, Z wave
  Bluetooth, Zigbee
  RFID
  Cellular channel
  PPP
  Sonet
  ATM, Frame Relay
  L2TP
  etc

## Slide 5: Connecting to a Server
Server
Connection to ISP

## Slide 6: What devices you use to connect to Internet?
WiFi Router
Connected to service
Providers eg Airtel
Over Fiber/Ethernet
ADSL Modem connected
to service provider over
Telephone line

## Slide 7: What devices you use to connect to Internet?
Use 3G/4G data-connection
Mobile Network

## Slide 8: What we have seen so far is at very high level … abstract view
What goes on underneath? How 0s and 1s are transmitted?

## Slide 9: To send a letter using postal service to your friend in some other city/Country, what do you need the most?

## Slide 10: A very Unique Postal Address of the Receiver

## Slide 11: Each sending and receiving machine must have unique IP address
The Internet too needs a uniquely defined addresses
IPv4 IP Address: 32 bits
#.#.#.#
4 numbers separated by .
Each number in the range: 0-255

## Slide 12: Each sending and receiving machine must have unique IP address
In your device, where does this IP address come from?
IPv4 IP Address: 32 bits
#.#.#.#
4 numbers separated by .
Each number in the range: 0-255

## Slide 13: Did you ever type these number like 10.200.128.66 in your laptop?
IPv4 IP Address: 32 bits
#.#.#.#
4 numbers separated by .
Each number in the range: 0-255

## Slide 14: DHCP Protocol provides IP address to your device ISP runs DHCP protocol Your Router also run DHCP Protocol
IPv4 IP Address: 32 bits
#.#.#.#
4 numbers separated by .
Each number in the range: 0-255
IPv6 is becoming popular .. Address size 128 bits

## Slide 15: Router first receives IP address from ISP for lease period using DHCP protocol Each device connected to the Router needs an IP address The DHCP Server in Router provides internal IP address to each device (using NAT)

## Slide 16: Each website run on a server (or servers) with an IP address
We use websites such as
Google.com, Amazon.com, facebook.com
We don’t specify ip address for google.com
So there must be translation between domain name and ip address

## Slide 17: Domain Name Server

## Slide 19
Your laptop shouts:
HEY, DOES WIRELESS NETWORK X EXIST?
1. Join the wireless network

## Slide 20
1. Join the wireless network
Wireless access point(s) continually shout: HEY, I’M WIRELESS NETWORK Y, JOIN ME!

## Slide 21
1. Join the wireless network
If either match up, your laptop joins the network. Optionally performs a cryptographic exchange.

## Slide 22
2. Configure your connection
Your laptop shouts:
HEY, ANYBODY, WHAT BASIC CONFIG DO I NEED TO USE?
I need IP address and
other parameters

## Slide 23
2. Configure your connection
Some system on the local network replies: Here’s your config, enjoy
DHCP server

## Slide 24
2. Configure your connection
The configuration includes:
An Internet address (IP address) your laptop should use; typ. 32 bits (IPv4). May also include 64b of the 128b IPv6 address
The address of a “gateway” system to use to access hosts beyond the local network
The address of a DNS server (“resolver”) to map names like google.com to IP addresses
192.168.1.14

## Slide 25
3. Find the address of google.com
Your laptop sends a DNS request asking: “address for google.com?”
It’s transmitted using the UDP protocol (lightweight, unreliable).
The DNS resolver might not be on the local network.
192.168.1.14

## Slide 26
gateway
3. Find the address of google.com
192.168.1.14

## Slide 27
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
3. Find the address of google.com
192.168.1.14

## Slide 28
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
google.com?
3. Find the address of google.com
192.168.1.14

## Slide 29
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
google.com?
(The resolver now itself uses DNS queries to other DNS servers to figure out the address associated with google.com.)
3. Find the address of google.com
192.168.1.14

## Slide 30
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
google.com’s address is 172.217.6.78
3. Find the address of google.com
192.168.1.14

## Slide 31
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
4. Connect to google.com server
192.168.1.14

## Slide 32: IP Packet Routing

## Slide 33: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization
Source: Kurose and Ross Book: 8th Edition

## Slide 34: Postal System Analogy

## Slide 36: Packet Routing
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router
Source: Kurose and Ross Book: 8th Edition

## Slide 37: End to End protocols

## Slide 38: Integrated view of the Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Source: Kurose and Ross Book: 8th Edition

## Slide 39: Service view of the Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
HTTP
Skype
Streaming
video
Source: Kurose and Ross Book: 8th Edition

## Slide 40: Thousands of Networking Applications
social networking
Web
text messaging
e-mail
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
P2P file sharing
voice over IP (e.g., Skype)
real-time video conferencing (e.g., Zoom)
Internet search
remote login
File transfer

## Slide 41: Website and Digital Transformation

## Slide 42: Website and Digital Transformation
A company’s website plays a critical role in it’s Digital Transformation
Most websites perform across multiple devices
  Desktops
  Mobiles
  Tablets, ipad
Website is any organization’s very important digital asset
  Needs to be well designed
As number of mobile and Internet users are growing, powerful website becomes vital
A website must meet existing and future business objectives
First contact point for customers

## Slide 43: Website – technical requirements
Designed to solve customer’s problems
Good integration with backend systems
  Servers, Server side logic, applications
  Databases, storages
  CRM
  Supply chain
  Data warehouses
  Payment systems, etc
Scalability
High Availability
High Agility
High Usability
Excellent UX design
Security

## Slide 44: Front-end and Back-end

## Slide 45: World Wide Web (www) - Basics

## Slide 46: The Web – History
World Wide Web (WWW): a distributed database of “pages” linked through Hypertext Transport Protocol (HTTP)
  First HTTP implementation - 1990
    Tim Berners-Lee at CERN
  HTTP/0.9 – 1991
    Simple GET command for the Web
  HTTP/1.0 –1992
    Client/Server information, simple caching
  HTTP/1.1 - 1996
Tim Berners-Lee
Source: Sylvia Ratnasamy, Course CS 166, Univ of California, Berkeley

## Slide 47: Web and HTTP
A web page consists of objects, each of which can be stored on different Web servers
Object can be HTML file, JPEG image, Java applet, audio file,…
Web page consists of base HTML-file which includes several referenced objects, each addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 48: Web Components
Client: web browsers, used to surf the Web
Server systems: used to supply information to these browsers
Computer networks: used to support the browser-server communication
  The Internet
Client
Server
Request “document A”
document A

## Slide 49: Web Components
Content:
  URL: naming content
  HTML: formatting content
Protocol for exchanging information: HTTP
Source: Sylvia Ratnasamy, Course CS 166, Univ of California, Berkeley

## Slide 50: Lecture - summary
The Internet plays a very crucial role in today’s businesses
The Internet runs over link layer technologies. Popular link layer technologies include: Ethernet, WiFi, and Cellular channels
To connect to any website (or any application), a laptop needs ip address
  DHCP server available in the local area network or outside, provides configuration parameters including ip address
To connect to a website, a laptop (or any other device) needs to resolve http address to ip address
  This is done using DNS – domain name server
Website of a business plays a very critical role in digital transformation

## Slide 51: Backup Slides

## Slide 52: HTTP overview
HTTP: hypertext transfer protocol
Web’s application-layer protocol
client/server model:
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
HTTP request
HTTP response
HTTP request
HTTP response
iPhone running
Safari browser
PC running
Firefox browser
server running
Apache Web
server

## Slide 53: HTTP overview (continued)
HTTP uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 54: Basics of the WWW
Hypertext: a format of information which allows one to move from one part of a document to another or from one document to another through hyperlinks
Uniform Resource Locator (URL): unique identifiers used to locate a particular resource on the network
Markup language: defines the structure and content of hypertext documents

## Slide 55: Static Web: HTML/XHTML, CSS
HTML stands for HyperText Markup Language
  It is a text file containing small markup tags that tell the Web browser how to display the page
XHTML stands for eXtensible HyperText Markup Language
  It is identical to HTML 4.01
  It is a stricter and cleaner version of HTML
CSS stands for Cascading Style Sheets
  It defines how to display HTML elements

## Slide 56: Why Programmability?
What’s the drawback to simple document model?
  Static

## Slide 57: Client-Side Programmability
Scripting language: a lightweight programming language
Browser scripting: JavaScript
  Designed to add interactivity to HTML pages
  Usually embedded into HTML pages
  What can a JavaScript Do?
    Put dynamic text into an HTML page
    React to events
    Read and write HTML elements
    Validate data before it is submitted to a server
    Create cookies
    …

## Slide 58: Server-Side Programmability
The requests cause the response to be generated
Server scripting:
  CGI/Perl: Common Gate Way Interface (*.pl, *.cgi)
  PHP: Open source, strong database support (*.php)
  ASP: Microsoft product, uses .Net framework (*.asp)
  Java via JavaServer Pages (*.jsp)
  …

## Slide 59: CGI
Common Gateway Interface:
  CGI provides a way by which a web server can obtain data from (or send data to) database, and other programs, and present that data to viewers via the web.
  A CGI program can be written in any programming language, but Perl is one of the most popular