## Slide 1: Lecture 5: Local Area Networks
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Contents
Computer + Telecommunication = Datacom / Network
Network Requirements for Digital Transformation
Different types of Datacom Technologies
LAN
Ethernet
Computer Network Top level view – Interplay with the Internet

## Slide 3: Computer and Communication Era begins
Great combination: Computing and Communication
  Computer Networks
    Wireline
    Wireless
Telecommuni
-catio
Computing
Computer
Network

## Slide 4: Network Requirements for Digital Transformation
High Connectivity
High bandwidth
Bandwidth on Demand
Real time communication – upper bound on delays
High Reliability
  Low error rate
  No packet loss
Manageability and Operation Support
  Ease of installation, Maintenance, Configurability
Network Agility - Adaption to changing business needs
Low cost – affordability
Security
Support for many low level protocols and technologies

## Slide 5: What are different types of Datacom technologies?

## Slide 6
Telnet
FTP
SMTP
DNS
DNS
TCP
UDP
IP
HTTP
Ether- net
DNS
ATM
DNS
FR
DNS
SONET
DNS
WiFi
DNS
PPP
DNS
GPRS
DNS
ARP
VPN
VLAN

## Slide 7: Datacom / Networking Protocols
Distributed Protocols
  Both ends of a wire or a path – run the same protocol
Hundreds of Networking Protocols
Many protocols are highly complex
  Example: GSM

## Slide 8: Today’s Network
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Source: Kurose and Ross Book: 8th Edition

## Slide 9: Local Area Network (LAN)

## Slide 10: Multiple ways of doing classification
Based on Locality
Local Area Network
Wide Area Network
Based on Access Technology
Wireline
Wireless
Based on Mobility
Non-mobile
Mobile

## Slide 11: Local Area Network and DT
Local Area Network - Pervasive
  Factories, Home, Offices, Shops, …even offices
Both wireline (Ethernet) and Wireless (WiFi)
Various Flavors of LAN
  Within Cars : Vehicle Area Network (VAN)

## Slide 12: Corporate Network

## Slide 13: In-Vehicle Network (VAN)
Ref: In-Vehicle Networking Solutions, Renesas
:

## Slide 14: Industrial Ethernet
Image credit: AutomationDirect.com :

## Slide 15: Many flavors of LANs
Ethernet IP
Powerlink
Ethercat
Wireless Sensor Network

## Slide 16: Local Area Network (LAN): Ethernet

## Slide 17: Ethernet: datalink layer technology
Ethernet dominated local-area networks for decades
Invented in 1973 @ Xerox. (IEEE 802.3)
Originally a LAN technology – now extended to MAN / WAN
Same frame format, different wiring schemes, data rates across generations

## Slide 18: Physical Media for Ethernet
Fiber
Wireless

## Slide 19: The Ethernet
The Ethernet is the most popular LAN technology
  Packet switching
History
  Developed by Bob Metcalfe and others at Xerox PARC in mid-1970s
  Roots in Aloha packet-radio network
  Standardized by Xerox, DEC, and Intel in 1978
  LAN standards define MAC and physical layer connectivity
    IEEE 802.3 (CSMA/CD - Ethernet) standard – originally 2Mbps
    IEEE 802.3u standard for 100Mbps Ethernet
    IEEE 802.3z standard for 1,000Mbps Ethernet
CSMA/CD Protocol
  Carrier Sense Multiple Access Collision Detection

## Slide 20: Ethernet Generations
Original Ethernet:
  Coaxial cable (10Base5)
  Thicknet.
Next Generation:
  Thin coax cable (10Base2)
  Thinnet.
Modern Ethernet:
  Twisted pair ethernet (10BaseT)
  Uses hub: physical star but logical bus.

## Slide 21: Ethernet Switches
active switch in center
each “spoke” runs a (separate) Ethernet protocol
  No collision
switch
bus: coaxial cable
star

## Slide 22: Gigabit Ethernet (1000 BASE X)
Provides speeds of 1000 Mbps (i.e., one billion bits per second capacity) for half-duplex and full-duplex operation.
Uses Ethernet frame format and MAC technology
  CSMA/CD access method with support for one repeater per collision domain.
  Backward compatible with 10 BASE-T and 100 BASE-T

## Slide 23: Gigabit Ethernet Technology
Gigabit Ethernet cabling.
1000 BASE SX fiber - short wavelength
1000 BASE LX fiber - long wavelength
1000 BASE CX copper - shielded twisted pair
1000 BASE T copper - unshielded twisted pair
Based on Fiber Channel physical signaling technology.

## Slide 24: Gigabit Ethernet

## Slide 25: Computer Network: Top level view

## Slide 26: Ethernet Segment
Ethernet segment consists of a collection of hosts connected by wires (twisted pairs) to a hub
Spans room or floor in a building
Operation
  Each Ethernet adapter has a unique 48-bit address (MAC address)
    E.g., 00:16:ea:e3:54:e6
  Hosts send bits to any other host in chunks called frames
  Hub slavishly copies each bit from each port to every other port
    Every host sees every bit
    Note: Hubs are on their way out. Bridges (switches, routers) became cheap enough to replace them (means no more broadcasting)
host
host
host
hub
100 Mb/s
100 Mb/s
port
Ref: Bryant and O’Hallaron, Book: Computer Systems: A Programmer’s Perspective

## Slide 27: Ethernet Segment : Switch
Ethernet Switches avoid packet collisions by avoiding unnecessary packet broadcasts
Learning switches – they learn about the location of hosts wrt port numbers
  Host 1 is connected to port 1
  Host 2 is connected to port 2
  Host 3 is connected to port 3
We will study evolution of Ethernet and CSMA/CD protocol, later.
host1
host2
host3
Switch
100 Mb/s
100 Mb/s
port
Ref: Bryant and O’Hallaron, Book: Computer Systems: A Programmer’s Perspective
Notes: Hubs are shared media devices. Everyone sees everyone’s packets, you’re only supposed to pay attention to those specifically directed to you, or to broadcasts. Not too secure, but cheap. Most wireless still qualifies as a “hub,” while actual wired ethernet hubs are becoming hard to find.
Switches aren’t shared, most of the time. The switch pays attention to the packets and makes a list of the “sender” ethernet addresses and makes a table (it removes old data after a while). When a packet comes along whose destination address is in the table (because that host has recently “talked” and identified itself) the packet only goes to that port. Unknown packets and broadcasts still go to all ports, but overall, there are nearly no collisions and is generally more secure. Switches are now much more common than hubs.

## Slide 28: Next Level: internets
Multiple LANs are connected by specialized computers called routers
The connected networks are called an internet – that uses TCP/IP
host
host
host
...
host
host
host
...
WAN
WAN
LAN 1 and LAN 2 might be completely different, totally incompatible
(e.g., Ethernet and Wifi, 802.11*, T1-links, DSL, …)
router
router
router
LAN1
LAN2
Adapted from: Bryant and O’Hallaron, Book: Computer Systems: A Programmer’s Perspective

## Slide 29: Logical Structure of an internet
Ad hoc interconnection of networks
  No particular topology
  Vastly different router & link capacities
Send packets from source to destination by hopping through networks
  Different packets may take different routes
  Routing protocols: BGP, OSPF, IS-IS
router
router
router
router
router
router
host
host

## Slide 30: Lecture Summary
Local Area Networks play a major role in overall world of networking
Ethernet is the de-facto standard for LAN
Extends from LAN to WAN to Mobile networking Infrastructure
Various flavors
  CAN
  Industry
  Office and Home
  Many other applications

## Slide 31: Elements of wireless Networks

## Slide 32: Elements of a wireless network
wired network
infrastructure
Book: Kurose and Ross: Wireless and Mobile Networks: 7- 32

## Slide 33: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!
Book: Kurose and Ross: Wireless and Mobile Networks: 7- 33

## Slide 34: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
Book: Kurose and Ross: Wireless and Mobile Networks: 7- 34

## Slide 35: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands
Book: Kurose and Ross: Wireless and Mobile Networks: 7- 35

## Slide 36: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router
Book: Kurose and Ross: Wireless and Mobile Networks: 7- 36

## Slide 37: IEEE 802.11 Wireless LAN
IEEE 802.11 standard | Year | Max data rate | Range | Frequency
802.11b | 1999 | 11 Mbps | 30 m | 2.4 Ghz
802.11g | 2003 | 54 Mbps | 30m | 2.4 Ghz
802.11n (WiFi 4) | 2009 | 600 | 70m | 2.4, 5 Ghz
802.11ac (WiFi 5) | 2013 | 3.47Gpbs | 70m | 5 Ghz
802.11ax (WiFi 6) | 2020 (exp.) | 14 Gbps | 70m | 2.4, 5 Ghz
802.11af | 2014 | 35 – 560 Mbps | 1 Km | unused TV bands (54-790 MHz)
802.11ah | 2017 | 347Mbps | 1 Km | 900 Mhz
all use CSMA/CA for multiple access, and have base-station and ad-hoc network versions
Book: Kurose and Ross: Wireless and Mobile Networks: 7- 37

## Slide 38: Lecture Summary

## Slide 39: Mobile World ..
Number of Mobile subscription > 6.8 Billion
  Number of mobile users: 4.1 Billion (60% of world’s population)
    No more growth in subscription in developed world (almost 110% coverage)
  75% GSM, 14% WCDMA/HSPA
  India : 884 Million subscribers (73% population) : source – TRAI
  Rapid growth expected in India, China, and developing countries
Mobile communication – Huge impact on our society – specially in developing countries
  Enabling a common man
  Significant impact on our productivity

## Slide 40: Fixed and Mobile Subscription
9,000
8,000
7,000
6,000
5,000
4,000
3,000
2,000
1,000
0
2016
2015
2014
2013
2012
2011
2010
2009
2008
Fixed broadband
Mobile PCs/tablets
Fixed narrowband voice
Fixed VoIP
Mobile subscriptions
Mobile broadband
Source: Ericsson (2011)
Mobile
Mobile
Broadband
Fixed Broadband
Voice
Mobile PC
Subscription In Million

## Slide 41: Nielsen's Law of Internet Bandwidth
Users' bandwidth grows by 50% per year
  10% less than Moore's Law for computer speed
  The new law fits data from 1983 to 2019